## Slide 1
定義
是一個單一產品的「規格」向量。定義為： ，其中 是 配色article number、 是尺寸 、 表示大人(ms)或小孩(jr)、而 是顏色。
是一個單一「訂單」向量。定義為，其中 是「規格」向量、 是 預期產量(Expected Volume)、 是出貨時間(Due Day)。
是一個單一「帶定價的訂單」向量，定義為，其中是訂單價格。
一個「帶定價的訂單」的集合。
是一個「機器狀態」的向量，定義為 ，其中MS是當前機台狀態（工作、換模、換色、損壞）、 是模具編號、 是尺寸、表示大人(ms)或小孩(jr)、 被分配到的訂單向量、 本輪製造數量(manufacturing volume)、T是累計利潤。
是一個機器狀態的集合。
Index 定義:
  : 帶價格的訂單
  : 製造輪次
  : 機台
（產品規格）
（訂單）=
（機台狀態）
=
（本輪次生產狀態）
以高定價訂單優先排輪次的概念，考慮最小的CT（生產高價值訂單並且機台狀況變化最小），將適合的訂單分配到每個機台上。
如果兩機台同分，則以累積利潤最大化方式排單。最後是隨機。
（更新）
（更新）
以「最大化生產訂單」與「最小化生產成本」為導向的多機台生產排程
（生產成本）
計算當每一個機台去生產每一個訂單，每個機台需要付出的代價（Cost）
以權重評分
（帶定價訂單）=
根據急單與否、生產便利性進行排序 ，使系統先排入定價高的訂單
以權重評分

## Slide 2
CAA 概念(數學推導)
Pseudocode:
計算
針對kk（優化次數）與r(輪次)的迴圈:
  在每一個「帶定價訂單」與機器狀態下，計算 。指定新的機器狀態，
  更新「帶價格的訂單」。
  計算機台利潤並予以累計
回到2，直到輪次結束
修改C和A的參數，使得i的數量變少, 最大化累計利潤與最小化機台更動。重新回到2計算新一輪的輪次表。
定義
是一個單一產品的「規格」向量。定義為： ，其中 是 配色article number、 是尺寸 、 表示大人(ms)或小孩(jr)、而 是顏色。
是一個單一「訂單」向量。定義為，其中 是「規格」向量、 是 預期產量(Expected Volume)、 是出貨時間(Due Day)。
是一個單一「帶定價的訂單」向量，定義為，其中是訂單價格。
一個「帶定價的訂單」的集合。
是一個「機器狀態」的向量，定義為 ，其中MS是當前機台狀態（工作、換模、換色、損壞）、 是模具編號、 是尺寸、表示大人(ms)或小孩(jr)、 被分配到的訂單向量、 本輪製造數量(manufacturing volume)、T是累計利潤。
是一個機器狀態的集合。
Index 定義:
  : 帶價格的訂單
  : 製造輪次
  : 機台
基本轉換：
面（原）料庫存(Inventory)： =是依照產品規格查詢原料庫存
工具（模具）庫存：
  ： 根據產品規格轉換出模具
  並且計算生產兩種產品之差異==(, , )
生產成本計算（Manufacturing cost）： ，當前輪次針對每一個I, k 計算生產成本。
分配方程
是從 方程中產生，而 則由產生。
(R for 獎勵)

## Slide 3
CAA concept (mathematical derivation)
Pseudocode:
Compute
Iteration for each round :
  Compute against all priced order and machine
  Assign new machine status
  Renew priced order
  Compute the
Back to 2, until the round stops
Modify the C and A function to optimize: min , max and , back to 2 to restart
Definition
as a single order vector, defined as , where is the specification vector, is the expected volume and is expected due day.
as the priced order vector, it is , as order price.
is a set of priced order.
as the specification of the product vector, defined as , where as article number, as size, as ms or jr, and as color number.
as machine status, defined as where SO is the Mold number, as size, as ms or jr , is the acquired priced order, is manufacturing volume at this round and as accumulated earning.
is set of machine
Index definition:
  : priced order index
  : manufacturing round
  : machine index
Basic conversion:
Inventory: = is the raw material in the stock, which can be manufactured.
Tool Inv:
  And ==(, , )
Manufacturing cost: as a real number for each , , and combination.
Assign function:
is generated by function and
(R for reward)

## Slide 4
CAA_USR
Base_Data_Folder
Current_working_Folder
WeightingFile_title() as string
WeightingFile_name() as string
CAA_const_structure
CAA_copyright
MultithreadSetting
KeyWindowStartPosition
CAA_initial_file
name+location
Some lib/func
標準後綴
Json R/W
CALA
Each setupfile should be defined one by one
CAA_general_func
CAA_USR_UI
CAA_ORDER
Implemented as OR
ORD()
SP (specification)
ART, SZ, MJ, CO
.import_OrderFile
.assign_Price
.update_Order
.export_ORDER
.import_ORDER
ORD (order)
SP
VE
DD
CAA_PriceNCostAssign
CAA_PriceNCost_Assign_UI
.Compute_Price_Wei_DueDay
.Compute_Price_Wei_MachineStatus
.Compute_Price_Wei_Inventory
.Compute_Price
.USR_read
.USR_write
.show_USR_folder
1 | Dueday(3):(a,b),weighting
2 | MachineStatus: (dCO, dSO, dSZ), weighting
3 | Inventory: (a,b), weighting
4 | MachineStatus (dCO, dSO, dSZ), weighting
5 | Previous Earning (dT), weighting
Weighting file id v.s. title
Format: (condition), weighting
CAA_WT (Weighting Table)
Name as string
FileName as string
FullFileName as string
ID as integer
lstCondition() as integer()
lstWeight() as double
.File_read
.File_write
MACH()
MACH (single machine)
MS,SO, SZ, MJ,CP,ORD,VM,T
CAA_MachineStatus
Implemented as MA
.import_MachineStatus_JSON
.import_MachineStatus_CSV
.export_MachineStatus, JSON
.export_MachineStatus_CSV
This is because, you got ORD inside, and ORD is an object, not a value
For the last machine status output
CAA_MatchingFunction
.matching1(MA,OR) as MA
CAA_Round
MA() as CAA_MachineStatus
OR() as CAA_ORDER
Round as integer
Max_Round as integer
CAA_Round_UI (Main)
MS as enum: manufacturing, Mold_change, down
.Compute_Cost_Wei_MachineStatus
.Compute_Cost_Wei_PreviousEarning
.Compute_Cost
CAA_Round_Matching
.gogo (computation entering point)
WeiTbl()

## Slide 5
CAA_USR
Base_Data_Folder
Current_working_Folder
WeightingFile_title() as string
WeightingFile_name() as string
CAA_const_structure
CAA_copyright
MultithreadSetting
KeyWindowStartPosition
CAA_const
CAA_profile_name
Some lib/func
attachDateTimeSurfix
CAA_JsonRW : with indented json string
CALA
Each setupfile should be defined one by one
CAA_general_func
CAA_USR_UI
CAA_ORDER
Implemented as OR
lstORD as list (of order)
SP (specification)
ART, SZ, MJ, CO
.import_OrderFile
.assign_Price
.update_Order
.export_ORDER
.import_ORDER
ORD (order)
SP
VE
DD
CAA_PriceNCostAssign
CAA_PriceNCost_Assign_UI
.Compute_Price_Wei_DueDay
.Compute_Price_Wei_MachineStatus
.Compute_Price_Wei_Inventory
.Compute_Price
.USR_read
.USR_write
.show_USR_folder
1 | Dueday(3):(a,b),weighting
2 | MachineStatus: (dCO, dSO, dSZ), weighting
3 | Inventory: (a,b), weighting
4 | MachineStatus (dCO, dSO, dSZ), weighting
5 | Previous Earning (dT1 dT2), weighting
Weighting file id v.s. title
Format: (condition), weighting
CAA_WT (Weighting Table)
Name as string
FileName as string
FullFileName as string
ID as integer
lstCondition() as integer()
lstWeight() as double
.File_read
.File_write
.normalization
MACH()
MACH (single machine)
MS,SO, SZ, MJ,CP,ORD,VM,T
CAA_MachineStatus
Implemented as MA
.import_MachineStatus_JSON
.import_MachineStatus_CSV
.export_MachineStatus, JSON
.export_MachineStatus_CSV
This is because, you got ORD inside, and ORD is an object, not a value
For the last machine status output
CAA_MatchingFunction
.matching1(MA,OR) as MA
CAA_Round
MA() as CAA_MachineStatus
OR() as CAA_ORDER
Round as integer
Max_Round as integer
CAA_Round_UI (Main)
MS as enum: manufacturing, Mold_change, down
CheckFolderExisted: 1=existed 2:notexisted, but add, 0: not existed,, added fail
CheckFolderSurfix check folder
.Compute_Cost_Wei_MachineStatus
.Compute_Cost_Wei_PreviousEarning
.Compute_Cost
CAA_Round_Matching
.gogo (computation entering point)
WeiTbl()
All path with “\” as surfix
Only 3 types, i put them in enum CAA.Weighting.CAA_weighting_Fromt
SZ: 4.5->45 13->130
MJ=0: JR, MJ=1: MS
Format: yyyyMMdd
dSP ( specification)
dART,dSZ, dMJ, dCO, same, dSZ_value
=false: it is different, =true: same
CAA_ARTCO
CAA, CO
.defineMEfromCSV
.defineMEFromJSON
.exportME2JSON
.exportME2CSV
.
lstARTCO
CAA_INVENTORY
lstINV as list (of INV)
.import_OrderFile
.assign_Price
.update_Order
.export_ORDER
.import_ORDER
INV: SP, VI
SOTOOL
SO, Sta(machineToolstatus)
lstSZ
UnitProducts,
SN1: the SIZE, start with 4,5,6, (the smllest size in integal)
SN2: the SN number against the number of TOOL, start with 1, 2,3,
.defineMeFromCSV
Public Enum MachineToolStatus
Available
InMaintainence
Down
Not_Available
Available_Plan_free
Available_Plan_inUse
End Enum
SO_ART_MJ
SO,
ART,
MJ
.defineMeFromCSV
.findSObyART as string
.findARTsbySO as string()
.findMachineStatus () as MachineToolStatus
.findAvailable() as Boolean
.recruitForProduction()
.releaseFromProduction()
Need update
CAA_SOARTMJ

## Slide 6
MACH()
MACH (single machine)
MS,SO, SZ, MJ,CP,ORD,VM,T
CAA_MachineStatus
Implemented as MA
.import_MachineStatus_JSON
.import_MachineStatus_CSV
.export_MachineStatus, JSON
.export_MachineStatus_CSV
This is because, you got ORD inside, and ORD is an object, not a value
For the last machine status output
CAA_INVENTORY
lstINV as list (of INV)
.import_OrderFile
.assign_Price
.update_Order
.export_ORDER
.import_ORDER
INV: SP, VI
CAA_OSTOOLs
OSTOOL
SO, Sta(machineToolstatus)
lstSZ
UnitProducts,
SN1: the SIZE, start with 4,5,6, (the smllest size in integal)
SN2: the SN number against the number of TOOL, start with 1, 2,3,
.defineMeFromCSV
Public Enum MachineToolStatus
Available: 0
InMaintainence : 1
Down: 2
Not_Available: 3
Available_Plan_free : 4
Available_Plan_inUse
End Enum
CAS_OSARTMJ
lstSO,
lstART,
.defineMeFromCSV
.findSObyART as string
.findARTsbySO as string()
.findMachineStatus () as MachineToolStatus
.findAvailable() as Boolean
.recruitForProduction()
.releaseFromProduction()
Need update
In the machinestatus, one should id which mold is in-use. As in the SN1 and SN2. if not assigned, the program will assign one to it.
This is color change
Public Enum MachineToolStatus
Available
InMaintainence
Down
Not_Available
Available_Plan_free = 100
Available_Plan_inUse = 150
Available_ToolChange1 = 200
Available_ToolChange2 = 250
Available_ToolChange3 = 300
End Enum
This is mold change
This is size change (no mold change)

## Slide 7
Machine view
Order view